InfluxDB Plug-in Configuration Guide
ELXS-ALL-UD-16-0002

# Installing the InfluxDB Plug-in

Extract the Mistral plug-ins archive that has been provided to you somewhere sensible. Please make sure that you use the appropriate version of the plug-ins for the architecture of the machine on which the plug-in will run.

In addition, if the Mistral Plug-ins package was obtained separately from the main Mistral product, please ensure that the version of the plug-in downloaded is compatible with the version of Mistral in use. Version 4.0 of the InfluxDB Plug-in as described in this document is compatible with Mistral v2.11.2 and above.

The InfluxDB plug-in can be found in, for example:

<installation directory>/output/mistral_influxdb_v4.0/x86_64/

for the 64 bit Intel compatible version, and in:

<installation directory>/output/mistral_influxdb_v4.0/aarch32/

for the 32 bit ARM compatible version.

The plug-in must be available in the same location on all execution hosts in your cluster.

# Configuring Mistral to use the InfluxDB Plug-in
Please see the Plug-in Configuration section of the main Mistral User Guide for full details of the plug-in configuration file specification. Where these instructions conflict with information in the main Mistral User Guide please verify that the plug-in version available is compatible with the version of Mistral in use and, if so, the information in the User Guide should be assumed to be correct.

## Mistral Plug-in Configuration File
The Mistral plug-in configuration file is an ASCII plain text file containing all the information required by Mistral to use any OUTPUT or UPDATE plug-ins required. Only a single plug-in of each type can be configured.

Once complete the path to the configuration file must be set in the environment variable MISTRAL_PLUGIN_CONFIG. As with the plug-in itself the configuration file must be available in the same canonical path on all execution hosts in your cluster.

This section describes the specific settings required to enable the InfluxDB Plug-in.

### PLUGIN directive
The PLUGIN directive must be set to “OUTPUT” i.e.

PLUGIN,OUTPUT

### INTERVAL directive
The INTERVAL directive takes a single integer value parameter. This value represents the time in seconds the Mistral application will wait between calls to the specified plug-in e.g.

INTERVAL,300

The value chosen is at the discretion of the user, however care should be taken to balance the need for timely updates with the scalability of the InfluxDB installation and the average length of jobs on the cluster.

### PLUGIN_PATH directive
The PLUGIN_PATH directive value must be the fully qualified path to the InfluxDB plug-in as described above i.e.

PLUGIN_PATH,<install_dir>/mistral_influxdb_v2.4/x86_64/mistral_influxdb

The PLUGIN_PATH value will be passed to /bin/sh for environment variable expansion at the start of each execution host job.

### PLUGIN_OPTION directive
The PLUGIN_OPTION directive is optional and can occur multiple times. Each PLUGIN_OPTION directive is treated as a separate command line argument to the plug-in. Whitespace is respected in these values. A full list of valid options for this plug-in can be found in section 2.2 Plug-in Command Line Options.

As whitespace is respected command line options that take parameters must be specified as separate PLUGIN_OPTION values. For example to specify the username the plug-in should use to connect to the InfluxDB server the option “-u username” must be provided, this must be specified in the plug-in configuration file as:

PLUGIN_OPTION,-u
PLUGIN_OPTION,username

Options will be passed to the plug-in in the order in which they are defined and each PLUGIN_OPTION value will be passed to /bin/sh for environment variable expansion at the start of each execution host job.

### END Directive
The END directive indicates the end of a configuration block and does not take any values.

## Plug-in Command Line Options
The following command line options are supported by the InfluxDB plug-in.

-d dbname, --database=dbname

Set the name of the database instance the plug-in should connect to. Defaults to “mistral”

-e filename, --error=filename

Set the location of the file which should be used to log any errors encountered by the plug-in. Defaults to sending messages to stderr for handling by Mistral.

-h hostname, --host=hostname

Set the location of the InfluxDB host the plug-in should connect to. Defaults to “localhost”

-m octal-mode, --mode=octal-mode

 Permissions used to create the error log file specified by the -e option.

-p passwd, --password=passwd

Set the password the plug-in should use to authenticate its connection to InfluxDB. Defaults to “” if the --user option is specified. If both the --user and --password options are unspecified the plug-in will attempt to initiate an unauthenticated connection.
-P number, --port=number

Set the port the plug-in should use for the connection. Defaults to “8086”

-s, --https

Use https to connect to InfluxDB rather than plain http.

-u username, --user=username

Set the username the plug-in should use to authenticate its connection to InfluxDB. Defaults to “” if the --password option is specified. If both the --user and --password options are unspecified the plug-in will attempt to initiate an unauthenticated connection.

-v var-name, --var=var-name

The name of an environment variable, the value of which should be stored by the plug-in. This option can be specified multiple times.

# Mistral’s InfluxDB data model
This section describes how the Mistral InfluxDB plug-in stores data within InfluxDB. It should be noted that there is some duplication of terminology between Mistral and InfluxDB.

## Measurements
Both products use the term “measurement”, in Mistral’s case this refers to the type of statistic being recorded e.g. bandwidth versus mean-latency, for InfluxDB it is the primary identifier of related data (analogous to a table in a standard RDBMS).

The use of this term by both products is closely enough aligned that the Mistral InfluxDB plug-in uses its measurement value as the measurement key that data is recorded under in InfluxDB. As such the term may be used interchangeably below.

The following is a list of all possible measurement values that can be produced by Mistral. As above where this list conflicts with information in the main Mistral User Guide please verify that the plug-in version available is compatible with the version of Mistral in use and, if so, the information in the User Guide should be assumed to be correct.

bandwidth	Amount of data processed by calls of the specified type in the time frame. This applies only to “read” and “write” calls.
count	The number of calls of the specified type in the time frame.
seek-distance	Total distance moved within files by calls of the specified type in the time frame. This applied only to “seek” calls.
max-latency	The maximum duration of any call of the specified type in the time frame. Subject to data sampling, see the Mistral User Guide for more information.
mean-latency	The mean duration of any call of the specified type in the time frame, provided the number of calls is higher than the value of MISTRAL_MONITOR_LATENCY_MIN_IO. Subject to data sampling, see the Mistral User Guide for more information.
total-latency	The total duration of time spent in calls of the specified type in the time frame, provided the number of calls is higher than the value of MISTRAL_MONITOR_LATENCY_MIN_IO. Subject to data sampling, see the Mistral User Guide for more information.

## Series Timestamps
Mistral produces log entries with time stamps to a precision of one microsecond. The Mistral InfluxDB plug-in will attempt to normalise any timezone information to derive the correct value for the “microseconds since epoch” required by InfluxDB.

## Tag Keys
The Mistral InfluxDB plug-in records log entries using the following Tag Keys

Tag Key	Tag Value Description
calltype	The list of call types specified in the log message CALL-TYPE field. The Mistral InfluxDB plug-in will always log compound types in alphabetical order. / E.g. if the log message listed call types as “read+write+seek” the plug-in will normalise this to “read+seek+write”
host	Copied from the log message HOSTNAME field with any domain component removed.
job-group	Copied from the log message JOB-GROUP-ID field unchanged or “N/A” if this field is blank.
job-id	Copied from the log message JOB-ID field unchanged or “N/A” if this field is blank.
label	Copied from the log message LABEL field unchanged.

In addition, if the plug-in is started with one or more --var options a tag key will be created for each of the environment variables specified and populated with the value detected when the plug-in is initialised. For example if the plug-in is started with the option --var=USER then a tag key USER will also be created and populated with the value of $USER read when the plug-in is started.

## Field Values
The Mistral InfluxDB plug-in records log entries using the following Field Values:

Tag Key	Tag Value Description
command	Copied from the log message COMMAND-LINE field unchanged.
cpu	Copied from the log message CPU field unchanged.
file	Copied from the log message FILE-NAME field unchanged.
logtype	Either “monitor” or “throttle” indicating the type of rule that generated the log.
mpirank	Copied from the log message MPI-WORLD-RANK field unchanged.
path	Copied from the log message PATH field unchanged.
pid	Copied from the log message PID field unchanged.
scope	Either “local” or “global” indicating the scope of the contract containing the rule that generated the log.
size-max	The upper bound of the operation size range as reported in the log message SIZE-RANGE field, converted into bytes. / If this field was set to “all” in the log message this value will be set to the maximum value of an “ssize_t”. This value is system dependent but for 64 bit machines this will typically be ﻿9223372036854775807.
size-min	The lower bound of the operation size range as reported in the log message SIZE-RANGE field, converted into bytes. / If this field was set to “all” in the log message this value will be set to “0”.
threshold	The rule limit as reported in the log message THRESHOLD field converted into the smallest unit for the measurement type. / For bandwidth rules this field will be bytes, for latency rules it is microseconds and for count rules the simple raw count.
timeframe	The timeframe the measurement was taken over as reported in the log message THRESHOLD field, converted into microseconds.
value	The measured value as reported in the log message MEASURED-DATA field converted into the smallest unit for the measurement type. / For bandwidth rules this field will be bytes, for latency rules it is microseconds and for count rules the simple raw count.

# Querying Mistral InfluxDB data
Although it is possible to query InfluxDB data directly the Mistral InfluxDB plug-in is packaged with a simple command line script mistral_query_influx.sh which can be used to identify jobs that have violated rules.

This script will return a list of job IDs and rule labels of InfluxDB log entries that satisfy the parameters provided.

The following command line options are supported by the mistral_query_influx.sh script.

-?, --help

Show a summary of the command line options available.

-c calltype, --call-type=calltype

Limit the query to the provided call type. The provided calltype value must be a valid combination of call types as described in the Mistral User Guide.

-d dbname, --database=dbname

Set the name of the database instance the script should connect to. Defaults to “mistral”

-f file, --filename=file

Limit the query to the provided filename. Used as a regular expression in a sub-string match.

-g groupid, --group=groupid

Limit the query to the provided job group ID.

-h hostname, --host=hostname

Set the location of the InfluxDB host the script should connect to. Defaults to “localhost”

-i pid, --pid=pid

Limit the query to the provided PID.

-j id, --job=id

Limit the query to the provided job ID.

-m measure, --measurement=measure

Type of rule to check. Must be a valid measurement type as describe in section 3.1 Measurements above. Defaults to “bandwidth”
-n num, --port=num

Set the port the script should use for the connection. Defaults to “8086”

-o cmd, --command=cmd

Limit the query to the provided command line. Used as a regular expression in a sub-string match.

-p file, --password=file

Filename that contains the connection password. Implies -u.

-q, --quiet

Suppress informative messages. If set the script will only output the list of job IDs and rule labels found.

-r label, --rule=label

Limit the query to the provided rule label.

-s, --ssl

Use https to connect to InfluxDB rather than plain http.

-t n[m|h], --time=n[m|h]

Limit the time period to check for rule violations to the last “n” minutes or hours. Must be specified in the format n[m|h] where 'n' is an integer which must be immediately followed by one of 'm' or 'h' indicating 'minutes' or 'hours' respectively. For example five minutes would be specified as "5m".

-u username, --user=username

Set the username the script should use to authenticate its connection to InfluxDB. If -p is not specified the user will be prompted for the password.

At least one of the options that limit the output of the query, -c, -f, -g, -i, -j, -o, -r, or -t, must be specified.

Output is a comma separated list of job IDs and the rule labels recorded with one record per line.